## Slide 1: Going Faster
Flight Planning, Time round TPs

## Slide 2: Agenda
After Briefing…
In and Out of a TP
Flight Analysis

## Slide 3: Briefing
So you get the weather and task. What next?
  Analyse
  Plan
  Backup plan…
  Be prepared to ignore the plan!
  15m Nats 2006

## Slide 4: Conclusions: Plan in Brifing
Start by thinking how fast you might go
  Go with your instincts.
  Use the calculator as a cross reference
Straddle 3pm with the task duration
  Vanilla day, max heating is 3pm, best part of the day
Then consider other factors
  Incoming weather for earlier starts
  End of Day affects; Lasham in a Southerly, Nympsfield in a SW breeze
  Pure Uncertainty- showers or not, do you believe the met
End up with an earliest and latest time to start

## Slide 5: Conclusions: Keep Adjusting, homing in
Keep thinking on the grid: Target time, Earliest/Latest
  Go back to the met, sat pics especially
  See how the day is developing compared with forecast
After launch, start to focus on target times
  Is it as good, better or worse
  Size up the competition, get into the pack, use them for information
  If people go early or hang back, make your own decision don’t just follow
Keep your Nerve and don’t crack
  Within a broad range any start time will be fine BUT
  Just going can be a tactical blunder as those behind pick you off
When you decide to start, go tactical
  Get into the very best position you can then start positively
  Take 5 minutes, 10 max but no more: start time is more important than 100ft more!

## Slide 6: In and Out of a TP

## Slide 7: Conclusions
You can really gain and lose a lot!
  Sharp turns at the TP with a breeze- plan early!
Keep flying through good air even close in
  Just routing a little can have a big affect
  Don’t fixate on the TP
Plan your route out as well as the way in
  Situational Awareness: angles, distances, options
  Think where you will go before you get to the TP
  Clouds will look different- sun and wind angles
Remember to stay away from the ground!
  It is fine going low round into wind TPs.
  But don’t land or get into survival mode!

## Slide 8: Intermission
After the Break: Flight Analysis

## Slide 9: Steve’s Flight
This was a good flight!
  Big distance in difficult conditions, much of it pretty quick
Got slow for some key reasons
  Spent more time in worse conditions
    North was worse, final glide late in the day
  Slow and cautious on the first run
    Wandered off in ‘long flight mode’
  Lots of weaving to search for lift
  Was slow to get going again after low points
  Was not able to find long runs in lift

## Slide 10: Steve’s What to Do
“Racing Mental Attitude” from the start
  Take a moment before starting: a turn or 5 just to get into gear
  Only go when you can see a good route out
Searching when low: if you don’t find it, probably not there
  Search positively then move on to the next cloud or source
  Never double back unless totally desperate!
Low points are history: plan the ahead not behind
  Once established climbing look around and decide what to do
  Climb right up if need be, be prepared to leave low and find better

## Slide 11: Regionals Day 3
Starting early on a good day?
  Usually a bad idea unless you can run a long way
  Try to keep your nerve and start with or behind
Adapt to Conditions as they come
  From good, through blue then overcast
  Be at a sensible height at transition: plan ahead!
Drive the glider for the day’s conditions
  4+kt thermals are GOOD. Push hard and keep going
  Accept weaker climbs only to avoid low point
  Stop at any height for 6kt on a 4kt day!