## Slide 1: Going Faster
Final Glides

## Slide 2: Agenda
What You Can Gain
What You Can Lose
Golden Rules of Final Glides
Flight Analysis
  Ian Reekie
  Alex Hipple
  Geoff Glasebroke
  Ryan Berry

## Slide 3: What you can Gain
Minimise the Inefficiency:
  Steepest glide angle, highest speed in straight line
  Ideally: follow similar achieved glide as rest of flight
    But only if you are totally mad!
Good final glides can win days
  Can gain several minutes by well judged final glides
  Leaving with enough height for safety
  Don’t pad your safety margin
Win and Lose competitions by 30s
  2 turns more/less on one final glide…

## Slide 4: 18m Day 4, top of last climb
Position at Start of FG
  25km behind front at 5k ft
  Last climb 4.7Kt, 63:1 to finish
Other glider positions
  48/8: higher, +5km
  LT: same height, 12k
What Happens
  Main pack climbs twice more
  Front runners get bogged and climb at 2-3Kt

## Slide 5: Everyone Stops at Didcot
Then catch up:
  Maintained height:
  Others stop to climb
Low gliders are covered
  630 climbs at 2.5kt
  LT at 40:1, 3.5k- should get back
Others stop in groups
  Two main gaggles
  Neither needed to stop

## Slide 6: Different Heights on final run home
Higher and Faster
  Safe but wasteful
  Not needed for big wings
Lower and Slower
  Conserving height
  Similar slope to G9
Performance Counts
  G9: Definite advantage at high speed
  105kph at top of last
  116kph at end of FG

## Slide 7: What you can Lose
Over-do it: climb away low and slow
  Maybe lose 5 minutes or more
  Worst case land out…
Or even…
  Blue, high, ‘safe’
  Lots of sink in streets
  Bicester from NW
    No option to get low
  Private accident…
    Rather than houses and play ground

## Slide 8: Undershooting
What is an Undershoot
  If you are getting back, into wind, but only just
  Get low and fast, out of wind gradient
How to do it:
  You must be sure you are getting back when you commit
  Get low- less than ½ wing span, then up smoothly over obstacles
  Push over gently to get ballistic trajectory (wing creates little lift)
Preparation before you Try
  Get into a 2 seater and try it out with an instructor!
  Be CERTAIN of field state and obstacles before doing for real
  Be SURE you are getting in- it makes a marginal glide safer…

## Slide 9: Golden Rules of Final Gliding
Look at fields near the site before you leave
  Know your options if it starts to go wrong
Never use speed to fly above 4kts
  Optimum high speed glide is 3kts StF
  No modern glider is efficient above that speed
Make it Safe at 2000ft AGL
  500ft in hand at chosen speed to fly; adjust speeds…
Keep Bigger Margins on Down Wind glides
  Tend to get worse glides down wind
Plan your finish at 5 minutes out
  Straight in or go round, which way, where to land
  Say what you are going to do.

## Slide 10: Conclusions
You can gain a LOT on final glides
  Start thinking Final Glide at least 1 full climb short
  Try to bounce it up but don’t ‘chase it’
  Great feeling when it works!
Keep your nerve but keep it safe
  Be safe at 2000ft, or stop and climb
  Be realistic about how it is working out
  Worst feeling ever- climbing at 1kt 15k short!